## Slide 1: Low-Boom Design and Analysis of a Blended-Wing-Body Configuration for Large-Sized Supersonic Transport
Lin Yi(presenter), Zhang Ke-shi, Han Zhong-hua, Chen Qing
1. Northwestern Polytechnical University, China
2. National Key Laboratory of Aircraft Configuration Design, China
Notes: Dear experts and colleagues
I am Lin Yi from Northwestern Polytechnical University.
It is a great honor to present our work today — "Low-Boom Design and Analysis of a Blended-Wing-Body Configuration for Large-Sized Supersonic Transport."

## Slide 2: Contents
Background & Motivation
Baseline Configuration
Low-Boom Design & Analysis
Conclusions & Outlook
Notes: My presentation consists of four parts:
first, research background and motivation;
second, generation of the baseline configuration;
third, low-boom design and analysis;
and finally, summary and outlook.

## Slide 3: 1. Background & Motivation
[1] Han et al., Sonic Boom Prediction and Low Sonic Boom Design Methods, Science Press, 2022.
[2] NASA Aeronautics Strategic Implementation Plan, 2023.
Boeing 787:
Mach 0.85
Supersonic transport:
Mach 2
Asia-Pacific 3-h circle
Global 1-day circle
Globalization demands efficient travel
New‑generation SSTs hold great promise for future civil aviation.
NASA 2023 strategic plan: "Efficient, economical and eco-friendly supersonic transport will be a gamechanger for intercontinental travel."
Notes: Faster travel improves the efficiency of global economic and cultural exchange.
Supersonic transport fly more than twice as fast as subsonic airliners and are regarded as a core technological frontier of the 21st-century aviation industry.
NASA's 2023 strategic plan states that "efficient, affordable, and environmentally friendly supersonic commercial transport will be a gamechanger for future intercontinental travel."
Supersonic transport is therefore one of the frontier topics in aviation.

## Slide 4: 1. Background & Motivation
Existing low‑boom concepts suffer from limited economic performance.
Loudness vs. seat capacity
Existing low‑boom concepts are generally limited to small‑PAX configurations. Economically, SST needs more than 50 seats to form a stable, profitable business model.
70
75
80
85
90
10
20
30
40
Loudness (PLdB)
Seats
NASA N+3: loudness ≤ 70 PLdB
NASA X-59
TsAGI Strizh
JAXA S4
LM QSTA
1 seat
75 PLdB
20 seats
78 PLdB
36 seats
85 PLdB
40 seats
80 PLdB
0
JSGD theoretical minimum boom vs. aircraft weight
Notes: However, strong sonic boom restricts the practical operation of supersonic transport.
To address this problem, many advanced low-boom configurations have been developed worldwide over the past decades, such as NASA's X-59, Lockheed Martin's QSTA, TsAGI's Strizh, and JAXA's S4.
We found that most of them have small capacity, they are all small bussiness jet.
Under the classical sonic boom theory, the theoretical minimum sonic‑boom level is strongly correlated with aircraft weight. It is evident that smaller‑capacity are more available for satisfying low‑boom constraints.
But, a smaller capacity usually means higher ticket fares, since the expensive operating cost of supersonic transport will spread over very few passengers.
In contrast, carrying more passengers per flight will significantly decreases the operating cost shared by each passenger, then the ticket fare will be reduced.

## Slide 5: 1. Background & Motivation
The low‑boom design space is constrained
What about upsizing the aircraft？
2 seats 1 row
4 seats 1 row
Redundant space
2× Passenger
4× Area
4× Volume
Area grows quadratically
Notes: So what about upsizing the aircraft?
This shows the cabin and fuselage cross‑section of a supersonic transport. Now if we double the number of seats, the fuselage cross‑sectional area will grow quadratically and have more redundant space.
Double passengers, 4 times area, 4 times volume, and in existing low-boom theory the volume is directly associated with the low boom target, if we need more fuselage volume for the cabin constraint, that means the low boom design space is significantly limited.
The key point is tranditional configuration's circular fuselage are poor at turning volume into passenger capacity. I call this volume efficiency, and it is low for tranditional configuration.
So what configuration gives us high volume efficiency?

## Slide 6: 1. Background & Motivation
4 seats 1 row
TAW
Configuration
BWB
Configuration
TAW
Configuration
BWB
Configuration
What about upsizing the aircraft？
Notes: Naturally we come out the Blended-Wing-Body configuration. BWB configuration are generally considered to have higher loading efficiency.

## Slide 7: 1. Background & Motivation
4 seats 1 row
More
redundant space
BWB features more lenient volume constraints
Fits the cabin
TAW
Configuration
BWB
Configuration
Notes: Let’s make a comparison. With 4 seats 1 row in both cases, the BWB configuration's cross-section better conforms to the cabin, and has less redundant space. Volume is converted more effectively into seating capacity.

## Slide 8: 1. Background & Motivation
This work: a 160-seat supersonic BWB (SBWB) configuration
1
Aerodynamic & sonic-boom characteristics analyze
2
Fore-body waveform design with classic JSGD inverse method
3
Rear-body waveform regulation: winglets and V-tails
Notes: Therefore, we proposes a 160-seat supersonic BWB configuration and systematically examines its feasibility and low-boom design potential through three tasks:
analyzing its aerodynamic and sonic boom characteristics;
performing forebody signature design with the classical JSGD inverse design method;
and studying the effects of winglet and V-tail on the aft body waveform.

## Slide 9: Contents
Background & Motivation
Baseline Configuration
Low-Boom Design & Analysis
Conclusions & Outlook

## Slide 10: 2. Baseline Configuration
Cabin Space Define
Notes: So, first we need to define the geometry of cabin so that we can establish the cabin constraint in subsequent design.
We set 40 rows with four seats per row to accommodate 160 passengers.
In a TAW configuration the cabin ceiling is curved and cannot serve as passenger space, so it is occupied by carry-on baggage.
In SBWB, a relatively complete rectangular cabin can be used: square overhead bins are more convenient, or the bins can be removed to give passengers more vertical space and improve comfort.

## Slide 11: 2. Baseline Configuration
SBWB configuration requires integrated design
Define the section shape by CST parameter
Generate aircraft geometry using NURBS surface generation method
Full-aircraft CST parameterization with cabin envelope constraint
(NURBS guarantees geometric smoothness)
Thin supersonic airfoil
Notes: For TAW configuration, the fuselage and wing are often designed separately. But the SBWB requires an integrated design.
So we use a full-aircraft CST parameterization method: all sections are parameterized by CST functions of the same order.
For the fuselage region, we fit CST parameters to enclose the predefined cabin. For the wing, CST parameters of thin supersonic airfoils are directly adopted.
Then adjacent sections are blended by third-order NURBS interpolation to construct the aerodynamic surface, NURBS method can guarantee the geometric smoothness.

## Slide 12: 2. Baseline Configuration
72m
2.1m
28m
half-model reference area = 400
Parameter | Value
Cruise Altitude | 18km
Cruise Mach Number | 1.8
Total Weight | 170t
Cruise Weight | 150t
Notes: Therefore we get the baseline configuration, Here presents the three‑view drawing.
The cruise condition is set at 18 km and Mach 1.8. The takeoff weight is 170 ton, with about 20 ton of fuel burned before entering cruise, giving a cruise weight of 150 ton.

## Slide 13: 2. Baseline Configuration
More uniform axial lift distribution
Baseline aerodynamic analysis
Baseline aerodynamic evaluation:
=4.1°, =0.107, L/D=11.2.
Pressure drag 62.2 %, viscous drag 37.8 %.
Notes: Then we performed a aerodynamic evaluation of the baseline configuration:
the cruise angle of attack is 4.1 degrees, the lift coefficient 0.107 and the lift-to-drag ratio is 11.2. By analyzing the drag components, it can be found that pressure drag accounts for 62.2% and viscous drag 37.8%, the drag is mainly volume-driven.
From the pressure distribution, the low-pressure region on the SBWB appears earlier than on the TAW configuration: the TAW adopts a sharp slender nose to control sonic boom, so lift only begins at wing, whereas the SBWB has more uniform axial lift distribution.

## Slide 14: 2. Baseline Configuration
Compressed aft taper → intense rear-body over-expansion
flat-top signature (volume–lift coupling) → split-design assumption invalid
Ground boom 105.7 PLdB ≈ Concorde;
Rear-body over-expansion is the primary barrier of the SBWB
Baseline sonic boom: 105.7 PLdB — rear-body over-expansion dominates
Near distribution
Near signature
Ground waveform
Notes: Now, analyse the sonic boom characteristics.
Constrained by the long cabin, the aft fuselage tapers sharply. This rapid volume drop creates strong over‑expansion at the aft‑body.
We extract the near‑field boom signature at three body lengths away.
We can see that SBWB produces a flat‑top forebody signature. This comes from its broader lift distribution and inherent volume‑lift coupling. that's also why we need integrated design method for SBWB.
Then we propagate this near‑field signature down to the ground, the undertrack boom reaches 105.7 PLdB — a level similar to Concorde.

## Slide 15: Contents
Background & Motivation
Baseline Configuration
Low-Boom Design & Analysis
Conclusions & Outlook
Notes: My presentation has four parts. I’ll first introduce the background and motivation, followed by the methodology and validation. Then, I’ll focus on the main results, and finally summarize the conclusions and future work.
Let me start with the background.

## Slide 16: 3. Low-Boom Design & Analysis
Classic JSGD works on SBWB — rear-body over-expansion remains
JSGD inverse design: 105.7PLdB → 99.2PLdB (−6.5PLdB)
near-signature comparison
Ground-waveform comparison
105.7PLdB
99.2PLdB
Shock peak caused by tail and wing
Notes: Next, the low-boom design, using the classical JSGD inverse design method on the full-aircraft parameterization.
After design, we get a new near‑field waveform, it has a strong nose shock and sloped mid‑waveform.
Propagation result shows that the ground sonic boom intensity is 99.2 PLdB. Compared with the baseline configuration, the boom level decreases by 6.5 PLdB. This indicates that the classical JSGD theory is still effective for the SBWB configuration.
However, the optimized configuration still maintains strong over‑expansion. From the ground waveform, aft‑body over‑expansion dominates the high sonic‑boom intensity.

## Slide 17: 3. Low-Boom Design & Analysis
Winglets and V‑tails provide aerodynamic control for BWB
Rear-body components: winglets ＆ V-tails
winglets geometry and dimensions
V-tails geometry and dimensions
V‑tail dimensions are determined by pitch and lateral‑directional moment requirements.
A large sweep angle is adopted to strengthen its influence on aft‑body wave‑system.
Notes: In previous low-boom design studies, those control surfaces like tail wing are generally used for regulating the aft-body waveform, we wondering if those components are also effective in SBWB.
We chose the winglets and V-tails because they are typical components usually adopted for BWB.
This shows the size and shape of the winglet and V-tail.
Without detailed flight mechanics analysis, its parameters are determined based on experience.
For the V-tail, its area is calculated according to pitch and lateral-directional moment requirements.
And a large sweep angle is specially designed to enhance its interference on the aft-body waveform.

## Slide 18: 3. Low-Boom Design & Analysis
Winglets suppress wing‑tip vortices thereby mitigate over‑expansion
Rear-body components I: winglets
Low pressure over the wing upper surface propagates to the aft‑body via wing‑tip vortices, amplifying aft‑body over‑expansion.
Winglets prevent this upper‑surface low‑pressure from intruding onto the lower‑surface.
Notes: First, the winglets.
For the mechanism: the low pressure over the wing upper surface propagates to the aft-body via the wing-tip vortices, amplifying the aft-body over-expansion.
The winglets prevent this upper-surface low pressure from intruding onto the lower surface.
So the wingtip vortices are suppressed, and the over-expansion is mitigated.

## Slide 19: 3. Low-Boom Design & Analysis
V‑tails are largely shielded by the fuselage, limiting their influence
Rear-body components I: V-tails
V‑tail effects are complex. They involve fuselage shielding and wing‑wave interference
This is preliminary work. V‑tail mechanisms are not systematically studied
Notes: Next, we install the V-tails.
From the pressure distribution, we can observe that shocks generated by the tail surfaces are shielded by the fuselage.
Comparing the near‑field signatures, we find the tail surfaces exert nearly no influence on the aft‑body wave system. This further demonstrates that most of the tail’s effect is shielded by the fuselage.
Althought V-tails have not show a effective influence in this case. but We must note that this is preliminary work, and the V-tail mechanisms are not systematically studied yet.

## Slide 20: 3. Low-Boom Design & Analysis
Component mutual interference: 99.2PLdB 98.7 PLdB
Rear-body components II: V-tails & combined installation
Aft‑body over‑expansion intensity is reduced.
Notes: Then, we install both components
The combined effect is not a simple superposition. The two components interfere with each other: the coupling further reduces the aft-body over-expansion, and the shock intensification from the winglets is also suppressed.
As the results show, the ground sonic boom intensity further reduced by 0.5 PLdB.

## Slide 21: Contents
Background & Motivation
Baseline Configuration
Low-Boom Design & Analysis
Conclusions & Outlook

## Slide 22: 3. Low-Boom Design & Analysis
Fore‑body: Try canards for potential waveform control
Rear‑body: Weaken volume‑termination shock by shaping the tail
Extension: Extend SBWB concept to supersonic business jets
Outlook
SBWB cabin‑conformal fuselage enlarges low‑boom design space
Classic JSGD method remains effective for sonic‑boom reduction on SBWB
Winglets and V‑tails enable regulation of aft‑body over‑expansion intensity
Conclusion
Notes: To conclude
First, the SBWB cabin-conformal fuselage enlarges the low-boom design space.
Second, the classic JSGD method remains effective for sonic-boom reduction on the SBWB.
Third, winglets and V-tails enable the regulation of the aft-body over-expansion intensity.
For future work, we will explore canard for fore‑body waveform control, adopt tail shaping to mitigate the over-expansion on the aft‑body, and further extend the SBWB concept to supersonic business jet applications.

## Slide 23
Thank you!
Questions are welcome
E-mail: linyi@mail.nwpu.edu.cn
Notes: Thank you for your attention. Questions are welcome!